Solar Water Heating – Functional Model

INITIAL BRIEF

Conceptual Statement

Need: To research, design, build and competitively test a Functioning Open Loop Solar Water Heating Model (Prototype) in order to evaluate the feasibility of constructing and installing a Solar Water Heating System for your own home.

Situational Issue: To heat hot water your own home consumes energy (typically electricity or gas) which is expensive.

Constraints: The Absorber Area is to be 40,000mm² (eg. 200mm x 200mm) and the Water Storage Vessel Volume is to be 500mL. Remaining constraints are listed in the Specifications.

Specifications

| Materials | Absorber Plate Copper 0.5mm Thickness Pipe/Tubing Copper – Manifold, Absorber & Pipework to storage to be to scale - gauged by the student – using the material options given Insulation Collector, Pipework & Water Storage Vessel to be insulated to prevent significant losses - to be determined by student from material options given |
| --- | --- |
| Joining | Joining Oxygen/Acetylene Gas Brazing Fasteners Consideration of couplings to be made but the expectation is that all joins will be permanent (no dismantling/servicing required) |
| Dimensions | Absorber Plate 40,000mm² Water Storage Vessel 500mL Angle Square to the Sun |
| Tolerances | Absorber Plate 40,000mm² +/- 800mm² (2%) Water Storage Vessel 500mL +/- 10mL (2%) Calculate & Determine Actual Volume of water in the entire system (piping/tubing/collector/storage vessel) |