## Slide 1: Yield Calculations
Material In | Weight In (kg) | Processing Step | Weight Out (kg) | Material out | Yield %
Whole fish | 100 | Fillet Mechanically debone, mince | 30 | Minced fish | 30%
Minced fish | 30 | Wash and press | 13.0 | Washed and pressed fish | 43%
Pressed fish Dry ingred water | 13 4.64 7.5 | Chopped, mix and boxed | 22.1 | Frozen fish blocks | 88%
Frozen blocks | 22.1 | Bandsawing | 21.2 | Frozen cubes | 96%
Frozen cubes | 21.2 | packaging | 17.4 | Packaged cubes | 82%

## Slide 2: Yield
Therefore from 100kg of fish received 17.4 kgs of fish cubes
Yield = 17.4/100 x 100 = 17.4%
Has large impact on product costings

## Slide 3: Mass Balance
Materials in | Weight (g) | Operation | Weight (g) | Materials Out
Lactose Glucose Salt Ginger Pepper Garlic Onion HVP Soy Sauce Paprika Red Wine MSG Sodium Bicarb Caramel Enzyme Keltrol Onion flakes | 3204 2220 1356 840 840 840 840 540 528 528 528 528 480 204 180 84 1260 | Blending And Filling | 13500 800 500 200 | Marinade In Sachets Mix left in ribbon Blender Mix on floor and Unusable sachets Samples
Total | 15 kg |  | 15 kg | Total

## Slide 4: Product Costing (1)
Use a spreadsheet so they can change the costing as they change the formulation or process
Can work out cost per unit, cost per batch and areas where cost can be reduced to meet key factors
Manufacturing costs
  Direct processing costs (variable)
  Fixed costs
  Plant overhead costs

## Slide 5: Product Costing (2)
Distribution and marketing costs
  Physical distribution costs
  Market channel costs
  Promotion costs
  Sales costs
Company costs
  Administration costs
  Working capital
  Development costs (including new equipment)
  Financing costs

## Slide 6: What Is Going to Be Important For Your Product?
Cooking times and temperature
Changes in viscosity
Filling temperature
pH
Yield (product, jar/bottles and labels)
Consistency
Product safety
Legal regulations